BIRLA INSTITUTE OF TECHNOLOGY AND SCIENCE

II SEMESTER 2016-2017

CE F342                   Water and Wastewater Treatment       Dated: 6.3.2017

Mid Semester Test (Closed Book)

Max. Marks: 90        							  Duration: 90 minutes

- A certain municipality in city A plans to use the water from river R as a raw water for a water treatment plant. Since the river is very turbid, pre-sedimentation is required. Hence a column test is carried out. The results of the column test are summarised below.                                [30]

| Time (min) | 0 | 60 | 80 | 100 | 130 | 200 | 240 | 420 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Concentration(mg/l) | 299 | 190 | 179 | 169 | 157 | 110 | 79 | 28 |

What is the percentage removal of particles if the hydraulic loading rate is 25 m³/m²- day? Sampling is done at a depth of 4 m.

- Determine the future population of a town by using Geometric increase method (to get the maximum population) and Incremental increase method, given the following data:                [15]

| Year | 1961 | 1971 | 1981 | 1991 | 2021 |
| --- | --- | --- | --- | --- | --- |
| Population in thousands | 93 | 111 | 132 | 161 | ? |

- Estimate the screen requirement for a plant treating a peak flow of 80 million litre per day of sewage. Assume that maximum velocity through screen is 0.8 m/s and angle of screen bar with horizontal is 500.Widh of screen is three times of its depth. Also calculate the head loss through the screen for fully cleaned and half clogged conditions.(Use rectangular bars with 1 cm width and 5 cm clear spacing).                                                                                                           [20]

- Explain the following with suitable sketches wherever necessary                                 [2x5=10]

a) BOD exertion as a function of de-oxygenation constant

b) Critical deficit

c) Self purification constant

d) Merits and demerits of alum as a coagulant

e) Hourly variation of water demand

5.   Write a short note on the following:                                                                          [4+4+2=10]

a)  Gravel bed aerator

b) Rotary drum strainer

c) Zone settling

6.    Describe the following                                                                                                         [3+2]

a) Bubble aeration has an advantage over falling droplets of water.

b) Narrow mixing channel with flume for coagulant mixing